## Slide 1: Project: Window Technology
Benefits:
HEALTH: Reduced drafting and improved daylight
COST: Reduce furniture fading and overall energy costs up to ~$400 per window per year
Image from Project
Background: The University of Minnesota has already researched window technology options in regards to efficiency. This information has been adapted to be specific for window selection in Searcy, AR.
Objectives:
A guide to choosing the most efficient and cost-effective window for White County affiliate Habitat for Humanity builds
Findings/Solutions:
Climate and Location
Orientation and Shading Conditions
  East and West sides of the house can cause an increase in energy costs
  Southern side easier to shade
Window Type
  Single hung with vinyl frame
  Currently using ThermaStar by Pella
Quality important for sustainability
  Harry G. Barr (Weather-barr)

## Slide 2: Project: Window Technology
Image from Project
U-Value:
Overall heat transfer coefficient
  Reciprocal of R-Value
  Measurement of thermal resistance
South-Central Region: U-Value ≤ 0.35
The larger the heating bill, the more important a low U-factor becomes
  Low U-factor is helpful during hot days to keep the heat out
SHGC:
Solar heat gain coefficient
  How well a window blocks solar heat
South-Central Region: SHGC ≤ 0.30
Lower SHGC values reduce summer cooling and overheating
  Low SHGC reduce free winter solar heat gain
Chart: Solar Heat Gain Coefficient Comparison
| 0.26 | 0.31000000000000016 | 0.41000000000000014 | 0.56000000000000005 | 0.7100000000000003
SHGC = 0.41 | 478.8152 | 503.2338 | 547.2048 | 649.8331 | 732.909
SHGC = 0.25 | 517.92 | 561.8911 | 613.2052 | 657.1762

## Slide 3: Project: Window Technology
Image from Project
Glazes:
Low thermal emissivity (Low-E) coating designed to allow visible light through and reflect the heat based on the wavelengths
Double glazing decreases energy costs $200/ year
Triple glazing decreases an additional $40/year
  Significantly decreases visible light entering the house
Chart: Glazing - Number of Coatings
Single | 706.0134 | 1412.0269 | 2118.0403 | 2824.0538 | 3530.0672 | 4236.0807 | 4942.0941 | 5648.1076 | 6354.121 | 7060.1345 | 7766.1479 | 8472.1614 | 9178.1748 | 9884.1883 | 10590.2017 | 11296.2152 | 12002.2286 | 12708.2421 | 13414.2555 | 14120.2689
Double | 517.92 | 1035.84 | 1553.7601 | 2071.6801 | 2589.6001 | 3107.5201 | 3625.4401 | 4143.3602 | 4661.2802 | 5179.2002 | 5697.1202 | 6215.0402 | 6732.9603 | 7250.8803 | 7768.8003 | 8286.7203 | 8804.6403 | 9322.5604 | 9840.4804 | 10358.4004
Triple | 478.8152 | 957.6303 | 1436.4455 | 1915.2607 | 2394.0758 | 2872.891 | 3351.7062 | 3830.5213 | 4309.3365 | 4788.1517 | 5266.9668 | 5745.782 | 6224.5972 | 6703.4123 | 7182.2275 | 7661.0427 | 8139.8578 | 8618.673 | 9097.4882 | 9576.3033

## Slide 4: Project: Window Technology
Image from Project
Chart: Total Costs - Initial Purchase and Energy Loss
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
ThermaStar: U - 0.31, SHGC - 0.3 | 994 | 1547 | 2100 | 2653 | 3206 | 3759 | 4312 | 4865 | 5418 | 5971 | 6524 | 7077 | 7630 | 8183 | 8736 | 9289 | 9842 | 10395 | 10948 | 11501 | 12054
Showcase: U - 0.35, SHGC - 0.22 | 630 | 1190 | 1750 | 2310 | 2870 | 3430 | 3990 | 4550 | 5110 | 5670 | 6230 | 6790 | 7350 | 7910 | 8470 | 9030 | 9590 | 10150 | 10710 | 11270 | 11830
Ply Gem: U - 0.30, SHGC - 0.22 | 938 | 1500 | 2062 | 2624 | 3186 | 3748 | 4310 | 4872 | 5434 | 5996 | 6558 | 7120 | 7682 | 8244 | 8806 | 9368 | 9930 | 10492 | 11054 | 11616 | 12178
JELD-WEN: U - 0.29, SHGC - 0.23 | 1589 | 2106 | 2623 | 3140 | 3657 | 4174 | 4691 | 5208 | 5725 | 6242 | 6759 | 7276 | 7793 | 8310 | 8827 | 9344 | 9861 | 10378 | 10895 | 11412 | 11929